## Slide 1: QoS-Aware In-Network Processing for Mission-Critical Wireless Cyber-Physical Systems
Qiao Xiang
Advisor: Hongwei Zhang
Department of Computer Science
Wayne State University
November 6th, 2012

## Slide 2: Introduction
Wireless Sensor Networks
  Highly resource-constrained
In-Network Processing
  Reduce traffic flow → resource efficient
  End-to-end QoS are usually not considered
Mission-Critical CPS:
  Close-loop control
  More emphasis on end-to-end QoS, especially latency and reliability

## Slide 3: Introduction
Packet packing
  Application independent INP
  Simple yet useful INP in practice
    UWB intra-vehicle control
    IETF 6LowPAN: high header overhead
Network coding
  First proposed in wireline networks
  Provide benefits on throughput and robustness

## Slide 4: Introduction
Our focus:
  Joint optimization between INP and QoS
  Understanding problem complexity
  Designing simple distributed online algorithm
  Explore systems benefits of different INP methods

## Slide 5: Roadmap
Real-time packet packing protocol
Proactive protection using network coding against single node failure
What is next?
  More generalized failure model, e.g., wireless jamming
  Combination of packet packing and inter-flow network coding

## Slide 6: Real-time packet packing
System Model
  A directed collection tree T = (V,E)
  Edge (vi, vj) ∈ E with weight ETXvi, vj (l)
  A set of information elements X = {x}
  Each element x: (vx, lx, rx, dx)
Problem (P):
  Schedule the transmission of X to R
  Minimize the total number of transmissions
  Satisfy the latency constraints of each x ∈ X

## Slide 7: Complexity Analysis
Problem P0
  Elements are of equal length
  Each node has at most one element
Problem P1
  Elements are of equal length
  Each node generates elements periodically
Problem P2
  Elements are of equal length
  Arbitrary data generating pattern

## Slide 8: Complexity Analysis
P0, P1, P2, P | K ≥ 3 | K = 2 | 
 |  | re-aggregation is not prohibited | re-aggregation is prohibited
Complexity | strong NP-hard | strong NP-hard | O(N3)
NP-hard to achieve approximation ratio |  |  | 
  K = Maximal packet length N = |X|
  Re-aggregation: a packed packet can be dispatched for further packing.

## Slide 9: Complexity Analysis
When K ≥ 3 and T is a tree, regardless of re-aggregation
  P0 is NP-hard →P1 is NP-hard → P2 is NP-hard → P is NP-hard
When K ≥ 3, and T is a chain, regardless of re-aggregation
  The reduction from SAT still holds*
When K = 2 and re-aggregation is not prohibited
  The reduction from SAT still holds in both tree and chain structures
When K = 2 and re-aggregation is prohibited
  Problem P is equivalent to the maximum weighted matching problem in an interval graph.
  Solvable in O(N3) by Edmonds’ Algorithm
  * This solves an open problem in batch processing

## Slide 10: A Utility Based Online Algorithm
Utility of holding a packet:
Utility of transmitting a packet:
Cost without packing
Cost with packing
Every packet received by parent can get fully packed via pkt

## Slide 11: A Utility Based Online Algorithm
Decision Rule
  The packet should be immediately transmitted if Up > Ul
  The packet should be held if Up ≤ Ul
Competitive Ratio
  Problem P’
    T is a complete tree
    Leaf nodes generate elements at a common rate
  Theorem: For problem P′, tPack is
-competitive, where K is the maximum number of information elements that can be packed into a single packet, V>1 is the set of nodes that are at least two hops away from the sink R.
  Example: When ETX is the same for each link, tPack is 2-comptetive

## Slide 12: Performance Evaluation
Experiment Setting Up
  Testbed: NetEye, a 130-sensor testbed
  Topology: 120 nodes, half are source nodes
  Protocols compared: noPacking, simplePacking, spreaded latency, common clock, tPack
  Traffic patterns: periodic traffic and event traffic
  Metrics:
    packing ratio
    delivery reliability
    delivery cost
    deadline catching ratio
    latency jitter

## Slide 13: 3 second packing ratio

## Slide 14: 3 second delivery reliability

## Slide 15: 3 second delivery cost

## Slide 16: 3 second deadline catching ratio

## Slide 17: 3 second latency jitter

## Slide 18: Proactive protection using random network coding
Network coding uses broadcast to increase network throughput.
Broadcast is natural in wireless networks.
Random network coding: coding vectors are randomly chosen from a finite field. Achieve the same throughput as deterministic network coding while easier to use.

## Slide 19: Motivation
Proactive protection: make sure the destination can always receive at least one copy of a packet even there is failure in the network.
In random network coding, every coded packet can be used for decoding at the destination, which has the potential for proactive protection.

## Slide 20: Motivation
In traditional 1+1 protection, i.e. two node-disjoint paths, the total transmission cost is approximately twice of single path routing.
The combination of opportunistic routing and random network coding has a higher throughput than single path routing, yet may introduce a higher transmission cost.

## Slide 21: Problem definition
Problem Q
  Given a DAG G = (V,E) with one source S and one destination T , find two node-disjoint sub-DAGs to deliver K linear independent packets to T in each sub-DAG using intra-flow random network coding with minimal total transmission cost.
Problem Q0:
  Given a DAG G = (V,E) with one source S and one destination T , find the optimal total transmission cost and the corresponding FCi for each node i to deliver K packets using intra-flow random network coding.

## Slide 23: An optimal solution to Q0

## Slide 25
Theorem 1. Algorithm 2 results in the optimal transmission cost and the corresponding topology in NC-based opportunistic routing.

## Slide 26: A heuristic solution to Q
Find 2 node-disjoint paths with minimal total cost
Assign other intermediate nodes into the two paths found earlier
Assignment rule: reduction of transmission cost of different decision

## Slide 28: Current progress
Studying the approximation ratio of the solution to problem Q
Implementing the protocol in tinyos-2.x

## Slide 29: What is next?
Compared with single node failures, protection against jamming is more important and complex.
  Proved its NP-hardness
  Exploring approximated solutions

## Slide 30
Both two INP are effective in reducing data traffic flow while providing QoS guarantee, what if they are utilized together?
  Packet packing is demonstrated in convergecast topology
  Intra-flow network coding can be designed to protect single flow
  Studying the combination of packet packing and inter-flow coding against failures in convergecast topology