## Slide 1: Searching for Stability in Interdomain Routing
Rahul Sami (University of Michigan)
Michael Schapira (Yale/UC Berkeley)
Aviv Zohar (Hebrew University)
Notes: Thank you..
Joint work with Schapira, Zohar; I’m going to present some results on stability in int routing

## Slide 2: Border Gateway Protocol (BGP)
Path-vector routing
Routing between Autonomous Systems
  ASes can apply routing policies
AT&T
Comcast
Akamai
Yahoo!
Notes: BGP – protocol used for inter d routing.
Routing between autonomous systs on the internet;
It is a path vector protocol; routers keep track of the available path to a given destination,
and the protocol is designed to allow Ases to express and
enforce routing policies: preferences for which route to select from all routes available to it
At a given point of time -> transition ->

## Slide 3: Convergence/Oscillation
Uncoordinated policies can lead to persistent global route oscillations
[Varadhan, Govindan, Estrin]
[Griffin, Wilfong], [Griffin, Shepherd, Wilfong]
  Several sufficient conditions for stable convergence [GR01, GGR01,GJR03,FJB05,..]
  open question: can a network have two stable solutions, but no oscillation?
Notes: The richness of the routing policy space – essentially, each AS can potentially pick an arbitrary ranking over the routes – comes with a cost.
It was first observed, by Varadhan et al, that uncoordinated choice of policies by different Ases can lead to persistent global oscillation. In other words,
It is possible for Ases to pick routing policies such that the routes do not reach a fixed point even when the network is fixed; instead, we could have a situation in which AS 1 picks a route, and then advertises it to its neighbors, who then change their routes, and advertise it on, and ultimately the cycle comes around.
Later, Griffin, Wilfong, and Shepherd formalized this path convergence problem: When does an instance of BGP – a network and a set of policy preferences – converge to a stable solution, and when does it oscillate?
Subsequently, there have been a number of papers presenting sufficient conditions for stable convergence. All of these sufficient conditions have had one feature – any instance satisfying these has had only one stable solution. However, from the work of Griffin et al, it has been an open question if this is really a necessary condition.
In other words, are their networks with multiple stable solutions, such that there is no persistent oscillation? This is in principle possible – regardless of where it starts out, the network can settle into one of the stable solutions.
->

## Slide 4: Our Results
Two stable solutions imply potential BGP oscillations
Notes: Our first result in this paper is to answer this open question negatively. We show that any network with two or more stable solutions implies the possiblility of persistent BGP oscillations. Thus, a particularly strong form of global coordination is required to ensure convergence if BGP is used for routing

## Slide 5: Our Results
Two stable solutions imply potential BGP oscillations
If preferences satisfy Gao-Rexford constraints
  Convergence of n AS network could require Ω(n) time in the wost case
  with α-level hierarchy, BGP converges after at most 2α+2 “phases”
Notes: Luckily, we believe that the Internet does have global structural properties that lead to stable convergence. In particular, Gao and Rexford introduced
a set of conditions that characterize actual ISP policies fairly well, and are sufficient to guarantee stable convergence. We ask a related question – how long does it take for BGP to converge in this setting?
We analyze this in a model with unrestricted asynchrony; we show that the worst case convergence time is quite bad – it could take Omega(n) time
However, a much tighter bound is possible in terms of another parameter – the length of the longest cust-provider chain (or, the number of tiers in a tiered ISP hierarchy). If this is alpha, we show that the worst case convergence time is roughly 2alpha timesteps.
In this talk, I will sketch the proof of the first result; due to the short time, I will not get into the running time results.

## Slide 6: BGP model: Routes and Preferences
Atomic AS/ representative router
Router state:
  Available routes to each destination
  Route preference rules
  Currently selected route
Abstract away export filters, MEDs, etc.
dest
route
AS1
AS1
AS1
AS2
AS3;AS1
AS27;AS3;AS1
AS8; AS4;AS1
AS4;AS2
…
Prefer AS27
Prefer shorter
…
Notes: I’ll begin by introducing our model of BGP dynamics.
We use a simplified model of BGP, that abstracts away many of the details and complexities of real-world BGP.
The biggest simplification is that we ignore intradomain structure altogether – we assume that each AS is an atomic entity,
Or equivalently, that all routers within an AS are identically configured.
In this setting, if we take a snapshot of what a router looks like at a particular point of time, it has two types of information.
Firstly, there is the policy information – the preference orders that the network operators of this AS have cinfigured onto the
Router.
Second, there is the information about currently available routes..

## Slide 7: BGP model: Dynamics
Each AS i actions:
  select best route from available routes
  advertise current route to neighbor j
Evolution governed by sequence of action events
Arbitrary (adversarial) timing, with two restrictions:
  Fair sequence (no starvation)
  Messages not delayed in transit (though may be dropped/lost)
(for any one destination)
i
j
k
Notes: That defines a snaphsot, now we’ll describe the evolution
Fix a dest. For any AS, there are two ..

## Slide 8: State-Transition Graphs
State: profile of all routers’ current routes and beliefs about their available routes
Transition: change following route selection or advertisement
*
Notes: The main technical tool we use in our analysis is the state transition graph, defined as follows.
A state is particular snapshot of the syst. State.
It includes a description of all routers’ current selected routes
Actions may change state
Not always – so self loops
Two specific kinds of state

## Slide 9: State-Transition Graphs
State: profile of all routers’ current routes and beliefs about their available routes
Transition: change following route selection or advertisement
*
* Zero state

## Slide 10: State-Transition Graphs
State: profile of all routers’ current routes and beliefs about their available routes
Transition: change following route selection or advertisement
*
* Zero state
Stable state(s)

## Slide 11: Main Proof sketch: Regions
Stable states: blue, red, …
Nonstable states:
  blue if all paths lead to blue stable state
  red if all paths lead to red stable state
  purple otherwise
*

## Slide 12: Proof Sketch: Confluence
Key lemma: from any purple state p, there is a (fair) path to another purple state
Proof:
  If all paths to red states, p would be red
  cannot have paths to both blue and red state:
  => must have path to some purple state p’
a
p
a
a
b
b
?
a,b : different actions

## Slide 13: Main result: Summary
If there are 2 or more stable states, zero state is purple
From every purple state, fair path to another purple state
Finite number of states=> must cycle sometime
=> BGP can oscillate on this instance!

## Slide 14: Convergence Time
Gao-Rexford conditions
  Assume: longest cust-prov chain length is α
Asynchronous model
  “Phase”: each router triggered at least once
Result: reach stable solution in at most 2α+2 phases

## Slide 15: Discussion & Future Work
Main result applies to [GSW] and other models
Average case instead of worst-case?
Compositional theory for safe policies?

## Slide 16
Thank you
Questions?